## Slide 1
SOBHA ACCEPTABLE QUALITY LEVEL (SAQL)
Document Title : | Silicon Application
Document Number : | SCL-SAQL-002
Date of Origin : | 08.05.2026
Date of Revision : | 
Revision Number : | 00
 | PREPARED BY | REVIEWED BY | REVIEWED BY | APPROVED BY | APPROVED BY | APPROVED BY | APPROVED BY
NAME | Mr. Deepan Shanmugavel | Mr. Rajeshkumar Lakshmanan | Mr. Thangapandi Rathinam | Mr. Suleyman Celik | Mr. Ayaz Siddiqui | Mr. Senthil Kumar Parasuraman | Mr. Karthikraj Rajendran
SIGNATURE |  |  |  |  |  |  | 
DATE |  |  |  |  |  |  | 

## Slide 2
AMENDMENT SHEET
DATE OF REV | SUBJECT OF THE AMENDMENT | REV. NO.
08/05/2026 | New release | 00
2

## Slide 3
OBJECTIVES
OBJECTIVE | The objective of this guideline is to provide a standard procedure for Silicon Application Acceptable levels according to the Zones.
SCOPE | This document is valid for Silicon Application Aesthetics Acceptance.
RESPONSIBLE | Site execution shall strictly adhere to the approved standards. QA/QC and QCS shall use these standards for inspection.
TERMS & REFERENCES | The QM / BE team shall be responsible for revising and updating the applicable standards as required.
3

## Slide 4
CATEGORIZATION / ZONES
Sobha Constructions LLC
4
Silicon Jamb External Facade
Silicon Jamb Internal Facade
Top
Bottom
Left
Right
Silicon – Façade Areas
Top
Bottom
Left
Right

## Slide 5
CATEGORIZATION / ZONES
Sobha Constructions LLC
5
Wardrobe
Silicon – Joinery Areas
Kitchen Cabinets
Door
Top
Bottom
Left
Right
Top
Left
Right
Top
Bottom
Bottom
Top
Left
Right
Right
Left

## Slide 6
CATEGORIZATION / ZONES
Sobha Constructions LLC
6
Silicon – Sanitary Areas
Sink and countertop bottom
Bath Tub
Shower Partition
Vanity Countertop
Top
Bottom
Top
Bottom
Top
Bottom
Top
Bottom
Left
Right
Left
Right
Right
Left
Left
Right

## Slide 7
Sobha Constructions LLC
7
SILICON ACTIVITY - SAQL
DEFECT DESCRIPTION / PARAMETER |  |  |  | Silicon Uneven Thickness (Façade Area) |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  | MEASURING METHOD |  |  |  |  | 
 |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  | German scale | Direct visual Inspection | 
 |  |  |  | STANDING POSITION |  |  | As required |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  | LIGHTING |  |  | Natural / Ambient light / Artificial Light |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Internal Jamb |  |  |  | External Jamb |  |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left
ACCEPTANCE LIMIT | Width :6,7,8,9,10 mm Allowed. Difference Between Side: Max 1mm Straighness:0mm on single side. | Width :6,7,8,9,10 mm Allowed. Difference Between Side: Max 1mm Straighness:0mm on single side. | Width :6,7,8,9,10 mm Allowed. Difference Between Side: Max 1mm Straighness:0mm on single side. | Width :6,7,8,9,10 mm Allowed. Difference Between Side: Max 1mm Straighness:0mm on single side. | Width :6,7,8,9,10 mm Allowed. Difference Between Side: Max 1mm Straighness:0mm on single side. | Width :6,7,8,9,10 mm Allowed. Difference Between Side: Max 1mm Straighness:0mm on single side. |  | Width :6,7,8,9,10 mm Allowed. Difference Between Side: Max 1mm Straighness:0mm on single side. | Width :6,7,8,9,10 mm Allowed. Difference Between Side: Max 1mm Straighness:0mm on single side.
REMARKS | Example : Left Side clearance shall be 7mm, and Right-Side clearance shall be 8,9mm. |  |  |  |  |  |  |  | 
Place the German scale flat against the wall end, ensuring it is properly seated.
Measure the thickness/offset up to the facade end by reading the scale at the contact point.
Measure the thickness and verify it against the specified tolerance.
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 8
Sobha Constructions LLC
8
SILICON ACTIVITY - SAQL
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Silicon Uneven Thickness (Joinery Area) |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  | German scale |  | Direct visual Inspection |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  | As required |  |  |  | 
APPLICABILITY |  |  VILLA  APARTMENT |  |  |  |  | LIGHTING |  |  |  | Natural / Ambient light / Artificial Light |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | All Wardrobe | All Wardrobe |  |  |  | All Kitchen Cabinets |  |  |  |  |  | All Doors |  |  | 
 | Top | Top | Bottom | Right | Left | Top |  | Bottom | Right | Left |  | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Width: 3,4mm Straightness: 0mm on single side. | Width: 3mm (+1/-0mm) Straighness:0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. |  | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. |  | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side.
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Place the German scale flat against the wall end, ensuring it is properly seated.
Measure the thickness of the silicon
Verify it against the specified tolerance.
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 9
Sobha Constructions LLC
9
SILICON ACTIVITY - SAQL
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  |  |  | Silicon Uneven Thickness (Sanitary Area) |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  | German scale |  |  |  |  | 
 |  |  |  |  |  |  |  |  | STANDING POSITION |  |  |  |  | As required |  |  |  |  | 
APPLICABILITY |  |  VILLA  APARTMENT |  |  |  |  |  |  | LIGHTING |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Bath Tub & Shower Partition | Bath Tub |  |  |  | Vanity Countertop & Sink Bottom |  |  |  |  | Tile Vs Skirting |  |  |  |  | Control Joint(Floor Tile) |  |  | 
 | Top | Top | Bottom | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Width: 3,4mm Straightness: 0mm on single side. | Width: 3mm (+1/-0mm) Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. | Width: 3,4mm Straightness: 0mm on single side. |  | Width: 3,4mm Straightness: 0mm on single side. | NA | Width: 4.8,4.9,5,5.1,5.2mm Straightness: 0mm on single side. | NA |  | NA | NA | Width: 1.3,1.4,1.5,1.6,1.7 mm Straightness: 0mm on single side. | NA | NA
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Place the German scale flat against the wall end, ensuring it is properly seated.
Measure the thickness of the silicon
Verify it against the specified tolerance.
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 10
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Uneven Silicone application |  |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  |  | Visual Inspection |  |  |  |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  |  |  | Minimum 1 Meter in any direction. |  |  |  |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  |  |  |  | LIGHTING |  |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Façade – Internal Jamb |  |  |  | Façade – External Jamb |  |  |  |  | Joinery |  |  |  |  | Sanitary |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Not allowed |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  | 
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SILICON ACTIVITY - SAQL
Visual inspection of painted areas shall be carried out under natural daylight or appropriate artificial lighting from all relevant directions.
10
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 11
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Silicone Undulations |  |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  |  | Visual Inspection |  |  |  |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  |  |  | Minimum 1 Meter in any direction. |  |  |  |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  |  |  |  | LIGHTING |  |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Façade – Internal Jamb |  |  |  | Façade – External Jamb |  |  |  |  | Joinery |  |  |  |  | Sanitary |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Not allowed |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  | 
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SILICON ACTIVITY - SAQL
Visual inspection of painted areas shall be carried out under natural daylight or appropriate artificial lighting from all relevant directions.
11
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 12
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Silicone damage |  |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  |  | Visual Inspection |  |  |  |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  |  |  | Minimum 1 Meter in any direction. |  |  |  |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  |  |  |  | LIGHTING |  |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Façade – Internal Jamb |  |  |  | Façade – External Jamb |  |  |  |  | Joinery |  |  |  |  | Sanitary |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Not allowed |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  | 
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SILICON ACTIVITY - SAQL
Visual inspection of painted areas shall be carried out under natural daylight or appropriate artificial lighting from all relevant directions.
12
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 13
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Silicone rough finish |  |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  |  | Visual Inspection |  |  |  |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  |  |  | Minimum 1 Meter in any direction. |  |  |  |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  |  |  |  | LIGHTING |  |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Façade – Internal Jamb |  |  |  | Façade – External Jamb |  |  |  |  | Joinery |  |  |  |  | Sanitary |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Not allowed |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  | 
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SILICON ACTIVITY - SAQL
Visual inspection of painted areas shall be carried out under natural daylight or appropriate artificial lighting from all relevant directions.
13
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 14
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Silicone shade variation |  |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  |  | Visual Inspection |  |  |  |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  |  |  | Minimum 1 Meter in any direction. |  |  |  |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  |  |  |  | LIGHTING |  |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Façade – Internal Jamb |  |  |  | Façade – External Jamb |  |  |  |  | Joinery |  |  |  |  | Sanitary |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Not allowed |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  | 
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SILICON ACTIVITY - SAQL
Visual inspection of painted areas shall be carried out under natural daylight or appropriate artificial lighting from all relevant directions.
14
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 15
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Uneven termination |  |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  |  | Visual Inspection |  |  |  |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  |  |  | Minimum 1 Meter in any direction. |  |  |  |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  |  |  |  | LIGHTING |  |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Façade – Internal Jamb |  |  |  | Façade – External Jamb |  |  |  |  | Joinery |  |  |  |  | Sanitary |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Not allowed |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  | 
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SILICON ACTIVITY - SAQL
Visual inspection of painted areas shall be carried out under natural daylight or appropriate artificial lighting from all relevant directions.
15
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 16
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Silicone peel-off |  |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  |  | Visual Inspection |  |  |  |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  |  |  | Minimum 1 Meter in any direction. |  |  |  |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  |  |  |  | LIGHTING |  |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Façade – Internal Jamb |  |  |  | Façade – External Jamb |  |  |  |  | Joinery |  |  |  |  | Sanitary |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Not allowed |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  | 
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SILICON ACTIVITY - SAQL
Visual inspection of painted areas shall be carried out under natural daylight or appropriate artificial lighting from all relevant directions.
16
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 17
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Silicone Discontinuous |  |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  |  | Visual Inspection |  |  |  |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  |  |  | Minimum 1 Meter in any direction. |  |  |  |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  |  |  |  | LIGHTING |  |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Façade – Internal Jamb |  |  |  | Façade – External Jamb |  |  |  |  | Joinery |  |  |  |  | Sanitary |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Not allowed |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  | 
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SILICON ACTIVITY - SAQL
Visual inspection of painted areas shall be carried out under natural daylight or appropriate artificial lighting from all relevant directions.
17
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 18
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Silicon Bubble formation |  |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  |  | Visual Inspection |  |  |  |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  |  |  | Minimum 1 Meter in any direction. |  |  |  |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  |  |  |  | LIGHTING |  |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Façade – Internal Jamb |  |  |  | Façade – External Jamb |  |  |  |  | Joinery |  |  |  |  | Sanitary |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | Not allowed |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  |  |  | Not allowed |  |  | 
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SILICON ACTIVITY - SAQL
Visual inspection of painted areas shall be carried out under natural daylight or appropriate artificial lighting from all relevant directions.
18
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 19
DEFECT DESCRIPTION / PARAMETER |  |  |  |  |  |  | Silicon Not in Line (Straightness) |  |  |  |  |  |  |  |  |  |  | 
DEFECT IMAGE / PARAMTER |  |  |  |  |  |  | MEASURING METHOD |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | INSTRUMENT / INSPECTION METHOD |  |  |  |  |  | German Scale |  |  |  |  | 
 |  |  |  |  |  |  | STANDING POSITION |  |  |  |  |  | As required |  |  |  |  | 
APPLICABILITY |  VILLA  APARTMENT |  |  |  |  |  | LIGHTING |  |  |  |  |  | Natural / Ambient light / Artificial Light |  |  |  |  | 
ACCEPTABLE QUALITY LEVEL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SCENARIO / LOCATION / ZONE | Façade – Internal Jamb |  |  |  | Façade – External Jamb |  |  |  |  | Joinery |  |  |  |  | Sanitary |  |  | 
 | Top | Bottom | Right | Left | Top | Bottom |  | Right | Left | Top | Bottom | Right |  | Left | Top | Bottom | Right | Left
ACCEPTANCE LIMIT | 0 mm |  |  |  | 0 mm |  |  |  |  | 0 mm |  |  |  |  | 0 mm |  |  | 
REMARKS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SILICON ACTIVITY - SAQL
Visual inspection of painted areas shall be carried out under natural daylight or appropriate artificial lighting from all relevant directions.
19
“Note: During keep-out inspection in case of any visual discrepancy identified, measurement verification shall be carried out based on the SAQL.”

## Slide 20
Thank you
In case any details are required, please contact the QM-QAQC@sobha-me.com .